## Slide 1: ADDRESSING MODES & Instruction set

## Slide 2: Introduction
8086 Microprocessor
Program
A set of instructions written to solve a problem.
Instruction
Directions which a microprocessor follows to execute a task or part of a task.
Computer language
High Level
Low Level
Machine Language
Assembly Language
 Binary bits
English Alphabets
‘Mnemonics’
Assembler Mnemonics  Machine Language

## Slide 3: Introduction
8086 Microprocessor
Program is a set of instructions written to solve a problem. Instructions are the directions which a microprocessor follows to execute a task or part of a task. Broadly, computer language can be divided into two parts as high-level language and low level language. Low level language are machine specific. Low level language can be further divided into machine language and assembly language.
Machine language is the only language which a machine can understand. Instructions in this language are written in binary bits as a specific bit pattern. The computer interprets this bit pattern as an instruction to perform a particular task. The entire program is a sequence of binary numbers. This is a machine-friendly language but not user friendly. Debugging is another problem associated with machine language.
To overcome these problems, programmers develop another way in which instructions are written in English alphabets. This new language is known as Assembly language. The instructions in this language are termed mnemonics. As microprocessor can only understand the machine language so mnemonics are translated into machine language either manually or by a program known as assembler.
Efficient software development for the microprocessor requires a complete familiarity with the instruction set, their format and addressing modes. Here in this chapter, we will focus on the addressing modes and instructions formats of microprocessor 8086.

## Slide 4: ADDRESSING MODES

## Slide 5: Addressing Modes
Group I : Addressing modes for register and immediate data
Group IV : Relative Addressing mode
Group V : Implied Addressing mode
Group III : Addressing modes for I/O ports
Group II : Addressing modes for memory data
8086 Microprocessor
Every instruction of a program has to operate on a data.
The different ways in which a source operand is denoted in an instruction are known as addressing modes.
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing

## Slide 6: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
The instruction will specify the name of the register which holds the data to be operated by the instruction.
Example:
MOV CL, DH
The content of 8-bit register DH is moved to another 8-bit register CL
(CL)  (DH)
Group I : Addressing modes for register and immediate data

## Slide 7: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In immediate addressing mode, an 8-bit or 16-bit data is specified as part of the instruction
Example:
MOV DL, 08H
The 8-bit data (08H) given in the instruction is moved to DL
(DL)  08H
MOV AX, 0A9FH
The 16-bit data (0A9FH) given in the instruction is moved to AX register
(AX)  0A9FH
Group I : Addressing modes for register and immediate data

## Slide 8: Addressing Modes : Memory Access
8086 Microprocessor
Physical Address (20 Bits)
Adder
Segment Register (16 bits)
0 0 0 0
Offset Value (16 bits)

## Slide 9: Addressing Modes : Memory Access
8086 Microprocessor
20 Address lines  8086 can address up to 220 = 1M bytes of memory
However, the largest register is only 16 bits
Physical Address will have to be calculated Physical Address : Actual address of a byte in memory. i.e. the value which goes out onto the address bus.
Memory Address represented in the form – Seg : Offset (Eg - 89AB:F012)
Each time the processor wants to access memory, it takes the contents of a segment register, shifts it one hexadecimal place to the left (same as multiplying by 1610), then add the required offset to form the 20- bit address
89AB : F012  89AB  89AB0 (Paragraph to byte  89AB x 10 = 89AB0)
F012  0F012 (Offset is already in byte unit)
+ -------
98AC2 (The absolute address)
16 bytes of contiguous memory

## Slide 10: Addressing Modes : Memory Access
8086 Microprocessor
To access memory we use these four registers: BX, SI, DI, BP
Combining these registers inside [ ] symbols, we can get different memory locations (Effective Address, EA)
Supported combinations:
[BX + SI] [BX + DI] [BP + SI] [BP + DI] | [SI] [DI] d16 (variable offset only) [BX] | [BX + SI + d8] [BX + DI + d8] [BP + SI + d8] [BP + DI + d8]
[SI + d8] [DI + d8] [BP + d8] [BX + d8] | [BX + SI + d16] [BX + DI + d16] [BP + SI + d16] [BP + DI + d16] | [SI + d16] [DI + d16] [BP + d16] [BX + d16]
BX BP | SI DI | + disp

## Slide 11: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Here, the effective address of the memory location at which the data operand is stored is given in the instruction.
The effective address is just a 16-bit number written directly in the instruction.
Example:
MOV BX, [1354H]
MOV BL, [0400H]
The square brackets around the 1354H denotes the contents of the memory location. When executed, this instruction will copy the contents of the memory location into BX register.
This addressing mode is called direct because the displacement of the operand from the segment base is specified directly in the instruction.
Group II : Addressing modes for memory data

## Slide 12: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In Register indirect addressing, name of the register which holds the effective address (EA) will be specified in the instruction.
Registers used to hold EA are any of the following registers:
BX, BP, DI and SI.
Content of the DS register is used for base address calculation.
Example:
MOV CX, [BX]
Operations:
    EA = (BX)
    BA = (DS) x 1610
    MA = BA + EA
    (CX)  (MA) or,
    (CL)  (MA)
    (CH)  (MA +1)
Group II : Addressing modes for memory data
Note : Register/ memory enclosed in brackets refer to content of register/ memory

## Slide 13: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In Based Addressing, BX or BP is used to hold the base value for effective address and a signed 8-bit or unsigned 16-bit displacement will be specified in the instruction.
In case of 8-bit displacement, it is sign extended to 16-bit before adding to the base value.
When BX holds the base value of EA, 20-bit physical address is calculated from BX and DS.
When BP holds the base value of EA, BP and SS is used.
Example:
MOV AX, [BX + 08H]
Operations:
    0008H  08H (Sign extended)
    EA = (BX) + 0008H
    BA = (DS) x 1610
    MA = BA + EA
    (AX)  (MA) or,
    (AL)  (MA)
    (AH)  (MA + 1)
Group II : Addressing modes for memory data

## Slide 14: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
SI or DI register is used to hold an index value for memory data and a signed 8-bit or unsigned 16-bit displacement will be specified in the instruction.
Displacement is added to the index value in SI or DI register to obtain the EA.
In case of 8-bit displacement, it is sign extended to 16-bit before adding to the base value.
Example:
MOV CX, [SI + 0A2H]
    Operations:
      FFA2H  A2H (Sign extended)
      EA = (SI) + FFA2H
      BA = (DS) x 1610
      MA = BA + EA
      (CX)  (MA) or,
      (CL)  (MA)
      (CH)  (MA + 1)
Group II : Addressing modes for memory data

## Slide 15: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In Based Index Addressing, the effective address is computed from the sum of a base register (BX or BP), an index register (SI or DI) and a displacement.
Example:
MOV DX, [BX + SI + 0AH]
    Operations:
      000AH  0AH (Sign extended)
      EA = (BX) + (SI) + 000AH
      BA = (DS) x 1610
      MA = BA + EA
      (DX)  (MA) or,
      (DL)  (MA)
      (DH)  (MA + 1)
Group II : Addressing modes for memory data

## Slide 16: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Employed in string operations to operate on string data.
The effective address (EA) of source data is stored in SI register and the EA of destination is stored in DI register.
Segment register for calculating base address of
source data is DS and that of the destination data is ES
    Example: MOVS BYTE
Operations:
Calculation of source memory location:
EA = (SI) BA = (DS) x 1610 MA = BA + EA
Calculation of destination memory location:
EAE = (DI) BAE = (ES) x 1610 MAE = BAE + EAE
(MAE)  (MA)
If DF = 1, then (SI)  (SI) – 1 and (DI) = (DI) - 1
If DF = 0, then (SI)  (SI) +1 and (DI) = (DI) + 1
Group II : Addressing modes for memory data
Note : Effective address of the Extra segment register

## Slide 17: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
These addressing modes are used to access data from standard I/O mapped devices or ports.
In direct port addressing mode, an 8-bit port address is directly specified in the instruction.
    Example: IN AL, [09H]
Operations: PORTaddr = 09H
(AL)  (PORT)
Content of port with address 09H is moved to AL register
In indirect port addressing mode, the instruction will specify the name of the register which holds the port address. In 8086, the 16-bit port address is stored in the DX register.
    Example: OUT [DX], AX
Operations: PORTaddr = (DX)
(PORT)  (AX)
Content of AX is moved to port whose address is specified by DX register.
Group III : Addressing modes for I/O ports

## Slide 18: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
In this addressing mode, the effective address of a program instruction is specified relative to Instruction Pointer (IP) by an 8-bit signed displacement.
Example: JZ 0AH
Operations:
  000AH  0AH (sign extend)
  If ZF = 1, then
  EA = (IP) + 000AH
  BA = (CS) x 1610
  MA = BA + EA
  If ZF = 1, then the program control jumps to new address calculated above.
  If ZF = 0, then next instruction of the program is executed.
Group IV : Relative Addressing mode

## Slide 19: Addressing Modes
8086 Microprocessor
Register Addressing
Immediate Addressing
Direct Addressing
Register Indirect Addressing
Based Addressing
Indexed Addressing
Based Index Addressing
String Addressing
Direct I/O port Addressing
10. Indirect I/O port Addressing
11. Relative Addressing
12. Implied Addressing
Instructions using this mode have no operands. The instruction itself will specify the data to be operated by the instruction.
Example: CLC
This clears the carry flag to zero.
Group IV : Implied Addressing mode

## Slide 20: INSTRUCTION SET

## Slide 21: Instruction Set
Data Transfer Instructions
Arithmetic Instructions
Logical Instructions
String manipulation Instructions
Process Control Instructions
Control Transfer Instructions
8086 Microprocessor
8086 supports 6 types of instructions.

## Slide 22: Instruction Set
1. Data Transfer Instructions
8086 Microprocessor
Instructions that are used to transfer data/ address in to registers, memory locations and I/O ports.
Generally involve two operands: Source operand and Destination operand of the same size.
Source: Register or a memory location or an immediate data
Destination : Register or a memory location.
The size should be a either a byte or a word.
A 8-bit data can only be moved to 8-bit register/ memory and a 16-bit data can be moved to 16-bit register/ memory.

## Slide 23: Instruction Set
1. Data Transfer Instructions
8086 Microprocessor
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
MOV reg2/ mem, reg1/ mem MOV reg2, reg1 MOV mem, reg1 MOV reg2, mem | (reg2)  (reg1) (mem)  (reg1) (reg2)  (mem)
MOV reg/ mem, data MOV reg, data MOV mem, data | (reg)  data (mem)  data
XCHG reg2/ mem, reg1 XCHG reg2, reg1 XCHG mem, reg1 | (reg2)  (reg1) (mem)  (reg1)

## Slide 24: Instruction Set
1. Data Transfer Instructions
8086 Microprocessor
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
PUSH reg16/ mem PUSH reg16 PUSH mem | (SP)  (SP) – 2 MA S = (SS) x 1610 + SP (MA S ; MA S + 1)  (reg16) (SP)  (SP) – 2 MA S = (SS) x 1610 + SP (MA S ; MA S + 1)  (mem)
POP reg16/ mem POP reg16 POP mem | MA S = (SS) x 1610 + SP (reg16)  (MA S ; MA S + 1) (SP)  (SP) + 2 MA S = (SS) x 1610 + SP (mem)  (MA S ; MA S + 1) (SP)  (SP) + 2

## Slide 25: Instruction Set
1. Data Transfer Instructions
8086 Microprocessor
Mnemonics: MOV, XCHG, PUSH, POP, IN, OUT …
IN A, [DX] IN AL, [DX] IN AX, [DX] | PORTaddr = (DX) (AL)  (PORT) PORTaddr = (DX) (AX)  (PORT)
IN A, addr8 IN AL, addr8 IN AX, addr8 | (AL)  (addr8) (AX)  (addr8)
OUT [DX], A OUT [DX], AL OUT [DX], AX | PORTaddr = (DX) (PORT)  (AL) PORTaddr = (DX) (PORT)  (AX)
OUT addr8, A OUT addr8, AL OUT addr8, AX | (addr8)  (AL) (addr8)  (AX)

## Slide 26: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
ADD reg2/ mem, reg1/mem ADC reg2, reg1 ADC reg2, mem ADC mem, reg1 | (reg2)  (reg1) + (reg2) (reg2)  (reg2) + (mem) (mem)  (mem)+(reg1)
ADD reg/mem, data ADD reg, data ADD mem, data | (reg)  (reg)+ data (mem)  (mem)+data
ADD A, data ADD AL, data8 ADD AX, data16 | (AL)  (AL) + data8 (AX)  (AX) +data16

## Slide 27: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
ADC reg2/ mem, reg1/mem ADC reg2, reg1 ADC reg2, mem ADC mem, reg1 | (reg2)  (reg1) + (reg2)+CF (reg2)  (reg2) + (mem)+CF (mem)  (mem)+(reg1)+CF
ADC reg/mem, data ADC reg, data ADC mem, data | (reg)  (reg)+ data+CF (mem)  (mem)+data+CF
ADDC A, data ADD AL, data8 ADD AX, data16 | (AL)  (AL) + data8+CF (AX)  (AX) +data16+CF

## Slide 28: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
SUB reg2/ mem, reg1/mem SUB reg2, reg1 SUB reg2, mem SUB mem, reg1 | (reg2)  (reg1) - (reg2) (reg2)  (reg2) - (mem) (mem)  (mem) - (reg1)
SUB reg/mem, data SUB reg, data SUB mem, data | (reg)  (reg) - data (mem)  (mem) - data
SUB A, data SUB AL, data8 SUB AX, data16 | (AL)  (AL) - data8 (AX)  (AX) - data16

## Slide 29: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
SBB reg2/ mem, reg1/mem SBB reg2, reg1 SBB reg2, mem SBB mem, reg1 | (reg2)  (reg1) - (reg2) - CF (reg2)  (reg2) - (mem)- CF (mem)  (mem) - (reg1) –CF
SBB reg/mem, data SBB reg, data SBB mem, data | (reg)  (reg) – data - CF (mem)  (mem) - data - CF
SBB A, data SBB AL, data8 SBB AX, data16 | (AL)  (AL) - data8 - CF (AX)  (AX) - data16 - CF

## Slide 30: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
INC reg/ mem INC reg8 INC reg16 INC mem | (reg8)  (reg8) + 1 (reg16)  (reg16) + 1 (mem)  (mem) + 1
DEC reg/ mem DEC reg8 DEC reg16 DEC mem | (reg8)  (reg8) - 1 (reg16)  (reg16) - 1 (mem)  (mem) - 1

## Slide 31: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
MUL reg/ mem MUL reg MUL mem | For byte : (AX)  (AL) x (reg8) For word : (DX)(AX)  (AX) x (reg16) For byte : (AX)  (AL) x (mem8) For word : (DX)(AX)  (AX) x (mem16)
IMUL reg/ mem IMUL reg IMUL mem | For byte : (AX)  (AL) x (reg8) For word : (DX)(AX)  (AX) x (reg16) For byte : (AX)  (AX) x (mem8) For word : (DX)(AX)  (AX) x (mem16)

## Slide 32: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
DIV reg/ mem DIV reg DIV mem | For 16-bit :- 8-bit : (AL)  (AX) :- (reg8) Quotient (AH)  (AX) MOD(reg8) Remainder For 32-bit :- 16-bit : (AX)  (DX)(AX) :- (reg16) Quotient (DX)  (DX)(AX) MOD(reg16) Remainder For 16-bit :- 8-bit : (AL)  (AX) :- (mem8) Quotient (AH)  (AX) MOD(mem8) Remainder For 32-bit :- 16-bit : (AX)  (DX)(AX) :- (mem16) Quotient (DX)  (DX)(AX) MOD(mem16) Remainder

## Slide 33: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
IDIV reg/ mem IDIV reg IDIV mem | For 16-bit :- 8-bit : (AL)  (AX) :- (reg8) Quotient (AH)  (AX) MOD(reg8) Remainder For 32-bit :- 16-bit : (AX)  (DX)(AX) :- (reg16) Quotient (DX)  (DX)(AX) MOD(reg16) Remainder For 16-bit :- 8-bit : (AL)  (AX) :- (mem8) Quotient (AH)  (AX) MOD(mem8) Remainder For 32-bit :- 16-bit : (AX)  (DX)(AX) :- (mem16) Quotient (DX)  (DX)(AX) MOD(mem16) Remainder

## Slide 34: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
CMP reg2/mem, reg1/ mem CMP reg2, reg1 CMP reg2, mem CMP mem, reg1 | Modify flags  (reg2) – (reg1) If (reg2) > (reg1) then CF=0, ZF=0, SF=0 If (reg2) < (reg1) then CF=1, ZF=0, SF=1 If (reg2) = (reg1) then CF=0, ZF=1, SF=0 Modify flags  (reg2) – (mem) If (reg2) > (mem) then CF=0, ZF=0, SF=0 If (reg2) < (mem) then CF=1, ZF=0, SF=1 If (reg2) = (mem) then CF=0, ZF=1, SF=0 Modify flags  (mem) – (reg1) If (mem) > (reg1) then CF=0, ZF=0, SF=0 If (mem) < (reg1) then CF=1, ZF=0, SF=1 If (mem) = (reg1) then CF=0, ZF=1, SF=0

## Slide 35: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
CMP reg/mem, data CMP reg, data CMP mem, data | Modify flags  (reg) – (data) If (reg) > data then CF=0, ZF=0, SF=0 If (reg) < data then CF=1, ZF=0, SF=1 If (reg) = data then CF=0, ZF=1, SF=0 Modify flags  (mem) – (mem) If (mem) > data then CF=0, ZF=0, SF=0 If (mem) < data then CF=1, ZF=0, SF=1 If (mem) = data then CF=0, ZF=1, SF=0

## Slide 36: Instruction Set
2. Arithmetic Instructions
8086 Microprocessor
Mnemonics: ADD, ADC, SUB, SBB, INC, DEC, MUL, DIV, CMP…
CMP A, data CMP AL, data8 CMP AX, data16 | Modify flags  (AL) – data8 If (AL) > data8 then CF=0, ZF=0, SF=0 If (AL) < data8 then CF=1, ZF=0, SF=1 If (AL) = data8 then CF=0, ZF=1, SF=0 Modify flags  (AX) – data16 If (AX) > data16 then CF=0, ZF=0, SF=0 If (mem) < data16 then CF=1, ZF=0, SF=1 If (mem) = data16 then CF=0, ZF=1, SF=0

## Slide 37: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 38: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 39: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 40: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 41: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 42: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 43: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 44: Instruction Set
3. Logical Instructions
8086 Microprocessor
Mnemonics: AND, OR, XOR, TEST, SHR, SHL, RCR, RCL …

## Slide 45: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
String : Sequence of bytes or words
8086 instruction set includes instruction for string movement, comparison, scan, load and store.
REP instruction prefix : used to repeat execution of string instructions
String instructions end with S or SB or SW. S represents string, SB string byte and SW string word.
Offset or effective address of the source operand is stored in SI register and that of the destination operand is stored in DI register.
Depending on the status of DF, SI and DI registers are automatically updated.
DF = 0  SI and DI are incremented by 1 for byte and 2 for word.
DF = 1  SI and DI are decremented by 1 for byte and 2 for word.

## Slide 46: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
REP REPZ/ REPE (Repeat CMPS or SCAS until ZF = 0) REPNZ/ REPNE (Repeat CMPS or SCAS until ZF = 1) | While CX  0 and ZF = 1, repeat execution of string instruction and (CX)  (CX) – 1 While CX  0 and ZF = 0, repeat execution of string instruction and (CX)  (CX) - 1

## Slide 47: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
MOVS MOVSB MOVSW | MA = (DS) x 1610 + (SI) MAE = (ES) x 1610 + (DI) (MAE)  (MA) If DF = 0, then (DI)  (DI) + 1; (SI)  (SI) + 1 If DF = 1, then (DI)  (DI) - 1; (SI)  (SI) - 1 MA = (DS) x 1610 + (SI) MAE = (ES) x 1610 + (DI) (MAE ; MAE + 1)  (MA; MA + 1) If DF = 0, then (DI)  (DI) + 2; (SI)  (SI) + 2 If DF = 1, then (DI)  (DI) - 2; (SI)  (SI) - 2

## Slide 48: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
CMPS CMPSB CMPSW | MA = (DS) x 1610 + (SI) MAE = (ES) x 1610 + (DI) Modify flags  (MA) - (MAE) If (MA) > (MAE), then CF = 0; ZF = 0; SF = 0 If (MA) < (MAE), then CF = 1; ZF = 0; SF = 1 If (MA) = (MAE), then CF = 0; ZF = 1; SF = 0 For byte operation If DF = 0, then (DI)  (DI) + 1; (SI)  (SI) + 1 If DF = 1, then (DI)  (DI) - 1; (SI)  (SI) - 1 For word operation If DF = 0, then (DI)  (DI) + 2; (SI)  (SI) + 2 If DF = 1, then (DI)  (DI) - 2; (SI)  (SI) - 2
Compare two string byte or string word

## Slide 49: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
SCAS SCASB SCASW | MAE = (ES) x 1610 + (DI) Modify flags  (AL) - (MAE) If (AL) > (MAE), then CF = 0; ZF = 0; SF = 0 If (AL) < (MAE), then CF = 1; ZF = 0; SF = 1 If (AL) = (MAE), then CF = 0; ZF = 1; SF = 0 If DF = 0, then (DI)  (DI) + 1 If DF = 1, then (DI)  (DI) – 1 MAE = (ES) x 1610 + (DI) Modify flags  (AL) - (MAE) If (AX) > (MAE ; MAE + 1), then CF = 0; ZF = 0; SF = 0 If (AX) < (MAE ; MAE + 1), then CF = 1; ZF = 0; SF = 1 If (AX) = (MAE ; MAE + 1), then CF = 0; ZF = 1; SF = 0 If DF = 0, then (DI)  (DI) + 2 If DF = 1, then (DI)  (DI) – 2
Scan (compare) a string byte or word with accumulator

## Slide 50: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
LODS LODSB LODSW | MA = (DS) x 1610 + (SI) (AL)  (MA) If DF = 0, then (SI)  (SI) + 1 If DF = 1, then (SI)  (SI) – 1 MA = (DS) x 1610 + (SI) (AX)  (MA ; MA + 1) If DF = 0, then (SI)  (SI) + 2 If DF = 1, then (SI)  (SI) – 2
Load string byte in to AL or string word in to AX

## Slide 51: Instruction Set
4. String Manipulation Instructions
8086 Microprocessor
Mnemonics: REP, MOVS, CMPS, SCAS, LODS, STOS
STOS STOSB STOSW | MAE = (ES) x 1610 + (DI) (MAE)  (AL) If DF = 0, then (DI)  (DI) + 1 If DF = 1, then (DI)  (DI) – 1 MAE = (ES) x 1610 + (DI) (MAE ; MAE + 1 )  (AX) If DF = 0, then (DI)  (DI) + 2 If DF = 1, then (DI)  (DI) – 2
Store byte from AL or word from AX in to string

## Slide 52: Instruction Set
Mnemonics | Explanation
STC | Set CF  1
CLC | Clear CF  0
CMC | Complement carry CF  CF/
STD | Set direction flag DF  1
CLD | Clear direction flag DF  0
STI | Set interrupt enable flag IF  1
CLI | Clear interrupt enable flag IF  0
NOP | No operation
HLT | Halt after interrupt is set
WAIT | Wait for TEST pin active
ESC opcode mem/ reg | Used to pass instruction to a coprocessor which shares the address and data bus with the 8086
LOCK | Lock bus during next instruction
5. Processor Control Instructions
8086 Microprocessor

## Slide 53: Instruction Set
6. Control Transfer Instructions
8086 Microprocessor
Transfer the control to a specific destination or target instruction
Do not affect flags
Mnemonics | Explanation
CALL reg/ mem/ disp16 | Call subroutine
RET | Return from subroutine
JMP reg/ mem/ disp8/ disp16 | Unconditional jump
8086 Unconditional transfers

## Slide 54: Instruction Set
6. Control Transfer Instructions
8086 Microprocessor
8086 signed conditional branch instructions
8086 unsigned conditional branch instructions
Checks flags
If conditions are true, the program control is transferred to the new memory location in the same segment by modifying the content of IP

## Slide 55: Instruction Set
6. Control Transfer Instructions
8086 Microprocessor
Name | Alternate name
JE disp8 Jump if equal | JZ disp8 Jump if result is 0
JNE disp8 Jump if not equal | JNZ disp8 Jump if not zero
JG disp8 Jump if greater | JNLE disp8 Jump if not less or equal
JGE disp8 Jump if greater than or equal | JNL disp8 Jump if not less
JL disp8 Jump if less than | JNGE disp8 Jump if not greater than or equal
JLE disp8 Jump if less than or equal | JNG disp8 Jump if not greater
8086 signed conditional branch instructions
8086 unsigned conditional branch instructions
Name | Alternate name
JE disp8 Jump if equal | JZ disp8 Jump if result is 0
JNE disp8 Jump if not equal | JNZ disp8 Jump if not zero
JA disp8 Jump if above | JNBE disp8 Jump if not below or equal
JAE disp8 Jump if above or equal | JNB disp8 Jump if not below
JB disp8 Jump if below | JNAE disp8 Jump if not above or equal
JBE disp8 Jump if below or equal | JNA disp8 Jump if not above

## Slide 56: Instruction Set
6. Control Transfer Instructions
8086 Microprocessor
Mnemonics | Explanation
JC disp8 | Jump if CF = 1
JNC disp8 | Jump if CF = 0
JP disp8 | Jump if PF = 1
JNP disp8 | Jump if PF = 0
JO disp8 | Jump if OF = 1
JNO disp8 | Jump if OF = 0
JS disp8 | Jump if SF = 1
JNS disp8 | Jump if SF = 0
JZ disp8 | Jump if result is zero, i.e, Z = 1
JNZ disp8 | Jump if result is not zero, i.e, Z = 1
8086 conditional branch instructions affecting individual flags

## Slide 57: Assembler directives

## Slide 58: Assemble Directives
8086 Microprocessor
Instructions to the Assembler regarding the program being executed.
Control the generation of machine codes and organization of the program; but no machine codes are generated for assembler directives.
Also called ‘pseudo instructions’
Used to :
› specify the start and end of a program
› attach value to variables
› allocate storage locations to input/ output data
› define start and end of segments, procedures, macros etc..

## Slide 59: Assemble Directives
8086 Microprocessor
Define Byte
Define a byte type (8-bit) variable
Reserves specific amount of memory locations to each variable
Range : 00H – FFH for unsigned value; 00H – 7FH for positive value and 80H – FFH for negative value
General form : variable DB value/ values
Example:
LIST DB 7FH, 42H, 35H
Three consecutive memory locations are reserved for the variable LIST and each data specified in the instruction are stored as initial value in the reserved memory location
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 60: Assemble Directives
8086 Microprocessor
Define Word
Define a word type (16-bit) variable
Reserves two consecutive memory locations to each variable
Range : 0000H – FFFFH for unsigned value; 0000H – 7FFFH for positive value and 8000H – FFFFH for negative value
General form : variable DW value/ values
Example:
ALIST DW 6512H, 0F251H, 0CDE2H
Six consecutive memory locations are reserved for the variable ALIST and each 16-bit data specified in the instruction is stored in two consecutive memory location.
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 61: Assemble Directives
8086 Microprocessor
SEGMENT : Used to indicate the beginning of a code/ data/ stack segment
ENDS : Used to indicate the end of a code/ data/ stack segment
General form:
Segnam SEGMENT … … … … … … Segnam ENDS | Program code or Data Defining Statements
User defined name of the segment
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM

## Slide 62: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM
Informs the assembler the name of the program/ data segment that should be used for a specific segment.
General form:
Segment Register
ASSUME segreg : segnam, .. , segreg : segnam
User defined name of the segment
ASSUME CS: ACODE, DS:ADATA | Tells the compiler that the instructions of the program are stored in the segment ACODE and data are stored in the segment ADATA
Example:

## Slide 63: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
FAR
NEAR
ENDP
SHORT
MACRO
ENDM
ORG (Origin) is used to assign the starting address (Effective address) for a program/ data segment
END is used to terminate a program; statements after END will be ignored
EVEN : Informs the assembler to store program/ data segment starting from an even address
EQU (Equate) is used to attach a value to a variable
ORG 1000H | Informs the assembler that the statements following ORG 1000H should be stored in memory starting with effective address 1000H
LOOP EQU 10FEH | Value of variable LOOP is 10FEH
_SDATA SEGMENT ORG 1200H A DB 4CH EVEN B DW 1052H _SDATA ENDS | In this data segment, effective address of memory location assigned to A will be 1200H and that of B will be 1202H and 1203H.
Examples:

## Slide 64: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
PROC Indicates the beginning of a procedure
ENDP End of procedure
FAR Intersegment call
NEAR Intrasegment call
General form
procname PROC[NEAR/ FAR] … … … RET procname ENDP | Program statements of the procedure Last statement of the procedure
User defined name of the procedure

## Slide 65: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
ADD64 PROC NEAR … … … RET ADD64 ENDP | The subroutine/ procedure named ADD64 is declared as NEAR and so the assembler will code the CALL and RET instructions involved in this procedure as near call and return
CONVERT PROC FAR … … … RET CONVERT ENDP | The subroutine/ procedure named CONVERT is declared as FAR and so the assembler will code the CALL and RET instructions involved in this procedure as far call and return
Examples:

## Slide 66: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
Reserves one memory location for 8-bit signed displacement in jump instructions
JMP SHORT AHEAD | The directive will reserve one memory location for 8-bit displacement named AHEAD
Example:

## Slide 67: Assemble Directives
8086 Microprocessor
DB
DW
SEGMENT
ENDS
ASSUME
ORG
END
EVEN
EQU
PROC
ENDP
FAR
NEAR
SHORT
MACRO
ENDM
MACRO Indicate the beginning of a macro
ENDM End of a macro
General form:
macroname MACRO[Arg1, Arg2 ...] … … … macroname ENDM | Program statements in the macro
User defined name of the macro